## Slide 1
CAPSTONE / IPR DISCLOSURE PRESENTATION
AIRLOCK
Context-Aware Automated Workstation Security & Autonomous Embedded Robotic Sentry Ecosystem
Multi-Tier Sensor Fusion | Adaptive Decision AI | Physical-Cyber Perimeter Defense
Inventors & Team: Akaash V P | Tejas Vasanth | Anirudh Narendran School of Computer Science and Engineering, VIT Chennai

## Slide 2
PROBLEM FORMULATION & REAL-WORLD THREAT
The Core Problem: The 15-Minute Vulnerability Gap
1. Static Inactivity Dilemma
• Conventional OS locks rely on fixed idle timers (5 to 15 minutes). • Users routinely step away without locking (meeting, coffee, printing). • Attacker needs only 15–30 seconds to inject a malicious USB payload, dump tokens, or compromise confidential files.
2. The Reading Lockout Trap
• Aggressive 60-second timeouts create unbearable cognitive friction. • Users reading technical specs or in discussion without touching the keyboard are falsely locked out. • Existing systems cannot differentiate between passive reading vs absent user.
3. Terminal State Fallacy
• Current security treats screen lock as a terminal state. • Once locked, the physical desk remains completely unattended and blind. • No mechanism detects, deters, or warns the owner when an unauthorized person approaches their locked desk.

## Slide 3
INNOVATIVE SOLUTION OVERVIEW
The AirLock Ecosystem: Cyber-Physical Synergy
A zero-trust cyber-physical defense loop connecting your smartphone, laptop OS, an intelligent decision pipeline, and an autonomous robotic desk sentry.
Pillar 1: Multi-Modal Fusion
• Asymmetric BLE Beacon: Phone broadcasts encrypted presence key without draining battery. • 1Hz OS Interrupt Hooks: Tracks mouse motion deltas and keystrokes. • Exponential Moving Average (EMA) filters RF multipath noise.
Pillar 2: Tri-Modal Decision AI
• Rule Engine: Instant microsecond decision for clear states (typing = WAIT). • Random Forest: Classifies tabular 7-feature context vectors (96.4% accuracy). • Gemini 1.5 Flash LLM: Resolves ambiguous 40-60% confidence edge cases.
Pillar 3: Active IoT Sentry
• Dual-Mode ESP32 Robot: Dormant during normal work; activates instantly upon OS lock. • Ultrasonic Perimeter: Detects desk intruders within 50 cm. • Cloud Verification: Interactive Telegram push asking owner: YES or NO.

## Slide 4
HARDWARE & SOFTWARE PIPELINE
System Architecture: Distributed Data & Control Plane
Mobile Key Subsystem
• Flutter Android App • BLE Peripheral Mode • Broadcasts 'AKAASH_KEY' • Interactive verification cards with instant action buttons • Telegram Bot Client
Desktop Sense-Decide Agent
• Python Bleak Bridge: Filters MAC & computes EMA smoothed RSSI • Electron + TypeScript Host: Samples keyboard/mouse 1Hz • LockService: Executes user32.dll!LockWorkStation • Local SQLite DB: Logs context & telemetry • Direct Hotspot Trigger: Pings bot over mDNS in <20ms
Embedded Robotic Sentry
• ESP32 Dual-Core SoC: Asynchronous HTTP WebServer • HC-SR04 Ultrasonic Transducer: 50 cm proximity monitoring • 4-State FSM: DORMANT -> SCANNING -> AWAITING -> ALARM • Active Deterrent: Piezo buzzer & strobe LEDs • Telegram Bot API Uplink

## Slide 5
OPERATIONAL STATE TRANSITIONS
End-to-End Execution Flow (Chronological Path)
Step 1: Normal Work
User at desk with phone. • RSSI: -54 dBm (Strong) • Keyboard/Mouse active • Decision: WAIT (Safe) • Bot: DORMANT (Silent)
Step 2: User Steps Away
User walks away (>2.5m). • RSSI drops past -78 dBm • Inactivity exceeds 3s • Decision Engine: LOCK (95% Conf) • Windows locks immediately
Step 3: Instant Arming
Sub-20ms Wakeup Signal. • Direct HTTP ping via hotspot: http://airlock-bot.local/start • Bot transitions to SCANNING mode • Ultrasonic sensor fires pulses
Step 4: Intruder Detected
Unauthorized person < 50cm. • Bot senses intrusion • Transitions to AWAITING_REPLY • Sends urgent Telegram alert with YES/NO action buttons
Step 5: Active Deterrent
Resolution or Sound Alarm. • User taps YES: Bot stands down • User taps NO or 30s timeout: Bot sounds 90dB buzzer + strobe LEDs to deter intruder

## Slide 6
CONTEXT INFERENCE & AMBIGUITY RESOLUTION
The 6-Stage AI Decision Pipeline
1
Stage 1: Deterministic Rule Engine — Microsecond execution of ground truth axioms: If user is actively typing/moving mouse, emit WAIT (90% conf). If idle > 3s AND RSSI < -75 dBm, emit LOCK (95% conf). Degrades gracefully without network.
2
Stage 2: Random Forest Classification — 7-Feature Vector: [idleTime, rssi, phoneMoving, keyboardActive, mouseActive, battery, charging]. Evaluates complex non-linear behavioral correlations trained on 10,000 synthetic context profiles.
3
Stage 3 & 4: Confidence Blending & Gating — Calibrates continuous probability distribution. Scores >= 70% execute immediate LOCK. Scores <= 35% execute WAIT. Uncertain cases routed to Stage 5.
4
Stage 5: Gemini 1.5 Flash LLM Fallback — Ambiguity Band (40% - 60% confidence): Queries Gemini API with prompt: 'Laptop idle {t}s, RSSI {r}, phone moving {m}, mouse inactive {i}. Recent corrections {p}. Should it lock?'. Solves subtle human edge cases in <800ms.
5
Stage 6: Adaptive Profile Personalization — Logs user false-positive overrides and feedback in SQLite to adaptively adjust individual user thresholds over time.

## Slide 7
PHYSICAL DEFENSE SUBSYSTEM
Embedded Robotic Sentry: Hardware & Cloud Verification
ESP32 Hardware Circuit & Specifications
• Microcontroller: ESP32 NodeMCU (240MHz Dual-Core, 520KB SRAM) • Ultrasonic Transducer: HC-SR04 - Trigger: GPIO 14 (10µs pulses every 150ms) - Echo: GPIO 27 (Time-of-flight echo return) - Effective Range: 2 cm to 400 cm (50 cm threshold) • Deterrents: Active Piezoelectric Buzzer (90 dB) & Flashing Warning LED (GPIO 26) • Networking: Wi-Fi 802.11 b/g/n + mDNS responder ('airlock-bot.local') • Power: Low quiescent dormant draw (<15mA when sleeping)
Dual-Channel Interactive Verification Loop
• Overcoming API Loop Limitation: Direct HTTP triggers wake the bot from the laptop in <20ms, bypassing Telegram's restriction on bot-to-bot messages. • User-Facing Telegram Bot Uplink: When intruder is detected within 50 cm: 1. Bot pings Telegram Chat ID directly over SSL. 2. Phone buzzes with immediate action options: [ YES, THAT'S ME ] -> Stands down to DORMANT [ NO, SOUND ALARM! ] -> Activates continuous alarm 3. 30-Second Fail-Safe: If owner doesn't reply in 30s, automatically triggers alarm to protect unattended desk.

## Slide 8
VALIDATION TESTBED RESULTS
Experimental Evaluation & Performance Metrics
2.4 sec
Average Lock Latency (vs 600s OS static timer)
96.4%
Model Decision Accuracy (Random Forest Classifier)
0.0%
False Lockout Rate During Active Reading
< 20 ms
Robot Arming Latency (Via Direct Hotspot HTTP)
Empirical Testing Scenarios (200 Test Trials)
• Active Typing (Phone at desk): 50/50 correct (100% precision) — zero false lockouts. • Passive Screen Reading (Zero mouse/keyboard input for 60s): 49/50 correct (98% precision) — holding beacon presence suppresses accidental lockout. • Normal Departure (User walks into hallway): 50/50 locked within 2.4s average. • Multipath RF Barrier Test (Walking behind concrete pillar): Signal decayed smoothly via EMA filter without false triggers. • Sentry Detection: 100% of physical desk intrusions within 50 cm prompted phone notification in < 1.2s.

## Slide 9
IPR & PATENT DISCLOSURE ANALYSIS
Patent Novelty & Technical Differentiation (< 35% Overlap)
Technology Dimension | Windows Dynamic Lock (US9781140B2) | Camera Gaze Systems (US10860714B2) | AirLock (Present Invention)
Decision Mechanism | Crude single RSSI threshold (binary disconnect) | Optical webcam eye gaze & facial presence | Tri-Modal Gating: Rule + Random Forest + Gemini LLM fallback
Lock Latency | 60 – 120 seconds (Extreme vulnerability gap) | 5 – 10 seconds (High CPU / GPU power drain) | 2.4 seconds average (Lightweight async event hooks)
False Lockout Immunity | Poor (Locks if phone moves slightly or RF fluctuates) | Poor (Fails in dark rooms or when user turns head) | Excellent (User peripheral interrupt override + EMA filter)
Post-Lock Physical Defense | None (Screen locks, desk left completely blind) | None (Camera goes dormant or locks OS only) | Active Autonomous IoT Sentry (Ultrasonic + Telegram Alert)

## Slide 10
INDUSTRIAL VALUE & ENTERPRISE SCALING
Market Potential & Commercial Applicability
Market Sizing & Growth Drivers
• Rapid Market Expansion: - 2024 Market Size: $2.8 Billion - 2030 Projected Size: $6.4 Billion - High Compound Growth Rate: 14.8% CAGR • Key Industry Drivers: - Clean-Desk Compliance: Mandatory regulations (ISO 27001, HIPAA, GDPR) with heavy fines for unattended open screens. - Hybrid Work & Hot-Desking: Shared co-working desks elevate physical compromise risks. - Physical Bad-Faith Attacks: Hardware USB Rubber Ducky and keystroke injection attacks require rapid physical counter-measures.
Commercial Adoption & Enterprise Deployment
• Target Licensing Companies: - Microsoft: Direct OS upgrade to Windows Dynamic Lock - Dell, HP, Lenovo: Pre-installed hardware security suite on commercial enterprise laptops - Cisco: Integrated zero-trust endpoint physical defense • Substantial Cost Advantage: - Traditional Enterprise Badges: $80 – $150 per seat - AirLock Architecture: Zero proprietary badge cost (uses existing smartphones + $5 IoT ESP32 sentry node) - Delivers a 90% reduction in endpoint hardware security costs.

## Slide 11
CONCLUSION
Summary of Contributions & Live Demonstration
Key Engineering Milestones Achieved
1. Proven Cyber-Physical Bridge: Demonstrated sub-2.5s workstation lockdown coupled with instant <20ms robotic physical sentry arming. 2. Robust Human-Context Sensing: Solved RF jitter and passive reading false-lockouts through EMA filtering and tri-modal ML/LLM confidence gating. 3. Cloud-Interactive Threat Mitigation: Built a dual-channel verification loop enabling real-time remote desk verification and deterrence via Telegram and Flutter. 4. Ready for Commercialization: TRL 4/5 working prototype with low hardware footprint and strong patentability profile.
Live Demonstration Overview
Demo Sequence for Evaluation: 1. At Desk: Phone nearby -> System active -> Bot DORMANT. 2. Walk Away: Signal drops -> Laptop locks -> Bot wakes up to SCANNING. 3. Intruder Approaches: Hand < 50cm -> Bot detects intrusion. 4. Telegram Push: Phone receives alert -> Tap YES (Stand down) or NO (Sound Alarm). Repository: github.com/tejasvasanth/sem7 (Branch: tejas)